## Slide 1
Hardware Components
For Automated Data Collection System
A Comprehensive Overview

## Slide 2
Vector Network Analyzer (VNA)
AURSINC NanoVNA-H vs Mini-VNA Tiny
Key Advantages of NanoVNA-H:
• Lower frequency coverage (10kHz)
• Standalone operation with built-in screen
• Portable data storage
• Active open-source community
• Significantly more cost-effective
Measurement Capabilities:
• S-parameters
• SWR (Standing Wave Ratio)
• Phase measurement
• Group delay analysis
• Smith Chart visualization
Notable Performance:
High-resolution sweep from 1 MHz to 20 MHz with 1568 steps
Feature | NanoVNA-H | Mini-VNA Tiny
Frequency Range | 10kHz - 1.5GHz | 1MHz - 3GHz
Built-in Display | Yes | No
Data Storage | MicroSD card slot | PC required
Cost | $35.99 | $522.13

## Slide 3
Microcontroller Comparison
Raspberry Pi 4 vs Arduino Uno
Key Advantages of Raspberry Pi 4:
• Superior processing power for complex computations
• Abundant memory for handling large datasets
• Full-fledged operating system for versatile development
• Extensive connectivity options for various peripherals
• Larger software ecosystem with numerous libraries
• Greater scalability for future project expansion
• Built-in Wi-Fi and Bluetooth for wireless capabilities
• HDMI output for easy monitoring and debugging
Feature | Raspberry Pi 4 | Arduino Uno
Processor | Quad-core Cortex-A72 64-bit @ 1.5GHz | ATmega328P @ 16MHz
RAM | 2GB, 4GB, or 8GB | 2KB SRAM
OS | Full Linux OS | Bare-metal
Connectivity | Ethernet, Wi-Fi, Bluetooth, USB 3.0 | Limited
GPIO Pins | 40 | 14 digital, 6 analog

## Slide 4
Sensors and Actuators
Temperature Sensor
• MAX31865 RTD Amplifier + PT100 Probe
• High-precision temperature readings
• SPI interface for Raspberry Pi connection
• Excellent noise immunity for accurate measurements
Angle Position Sensor
• BNO055 Absolute Orientation Sensor
• Accurate tilt and orientation data
• I2C interface for easy Raspberry Pi integration
• Built-in sensor fusion for reliable readings
Stepper Motor System
• NEMA 17 Stepper Motor + A4988 Driver
• Enables precise automated angle adjustments
• GPIO-controlled via Raspberry Pi
• Microstepping for smooth and accurate positioning

## Slide 5
System Setup and Integration
Hardware Integration Steps:
1. Connect NanoVNA-H to Raspberry Pi USB port
• Ensure proper driver installation for communication
2. Wire MAX31865 RTD Amplifier to Raspberry Pi SPI pins
• Configure SPI interface in Raspberry Pi settings
3. Connect BNO055 sensor to Raspberry Pi I2C pins
• Enable I2C in Raspberry Pi configuration
4. Link A4988 stepper driver to GPIO pins for NEMA 17 control
• Set up proper current limiting for the stepper motor
5. Assemble all components in a suitable enclosure
• Ensure proper ventilation and cable management

## Slide 6
Software Architecture
Core Functionality
• Sensor and VNA initialization routines
• Continuous data collection loop:
• Temperature readings (MAX31865)
• VNA data acquisition (NanoVNA-H)
• Orientation data (BNO055)
• Precise timestamp logging
• Automated stepper motor adjustments
Key Features
• Fully automated data collection process
• Synchronized multi-sensor timestamps
• Programmed angle adjustments for comprehensive measurements
Robust error handling and data validation
Recommended Python Libraries
• python-nanovna: NanoVNA-H interface and control
• adafruit-circuitpython-max31865: Temperature sensor management
• adafruit-circuitpython-bno055: Orientation sensor integration
• RpiMotorLib: Stepper motor control and positioning